## Slide 1
Tentative schedule
If you have questions, I am in room 1A-69
Today (July 23)
Introduction and
Sediment characterization
Tomorrow (July 24)
Brief review of open channel flow
Exner equation
July 27 (Monday)
Initiation of motion
July 28 (Tuesday)
Fluvial bedforms (intro)
July 29 (Wednesday)
Flow resistance
Foundations of stability analysis
July 30 (Thursday)
Bedload transport
July 31 (Friday)
Bedload transport
Stability analysis of fluvial bars
August 3 (Monday)
Seminar
Stability analysis of dunes
August 4 (Tuesday)
Total load calculations
August 5 (Wednesday)
Suspended load calculations
Weakly nonlinear stability analysis

## Slide 2
Various
Main reference
Gary Parker’s e-book 1D Sediment Transport Morphodynamics with applications to rivers and turbidity currents. Freely downloadable at http://hydrolab.illinois.edu/people/parkerg/morphodynamics_e-book.htm
Voluntary group work
viparell@cec.sc.edu or eviparelli@gmail.com or eviparelli@unina.it

## Slide 3
Sediment
Boulders
Pebbles / cobbles
Gravel
Coarse sand
Fine sand
Silt
Clay

## Slide 4
Sediment size (diameter D)
Boulders
(D > 256 mm)
Pebbles / cobbles
(D = 64 mm – 256 mm)
Gravel
(D = 2 mm – 64 mm)
Coarse sand
Fine sand
Silt
(D = 0.002 mm – 0.0625 mm)
Clay
(D < 0.002 mm)
Sand (D = 0.0625 mm - 2 mm)

## Slide 5
Sediment size (diameter D)
Boulders
(D > 256 mm)
Pebbles / cobbles
(D = 64 mm – 256 mm)
Gravel
(D = 2 mm – 64 mm)
Coarse sand
Fine sand
Silt
(D = 0.002 mm – 0.0625 mm)
Clay
(D < 0.002 mm)
Sand (D = 0.0625 mm - 2 mm)
6 orders of magnitude
properties and transport
way to compare sediment sizes

## Slide 6
properties and transport
way to compare sediment sizes
Sediment size (diameter D)
Boulders
(D > 256 mm)
Pebbles / cobbles
(D = 64 mm – 256 mm)
Gravel
(D = 2 mm – 64 mm)
Coarse sand
Fine sand
Silt
(D = 0.002 mm – 0.0625 mm)
Clay
(D < 0.002 mm)
Sand (D = 0.0625 mm - 2 mm)
6 orders of magnitude
COHESIVE
electrochemical forces between particles

## Slide 7
Bed material and wash material
Bed material forms the bed and lower banks of the river. It chiefly determines channel morphology. In alluvial channels, it corresponds with the coarser part of the sediment load (Church, 2006).
Wash material once entrained is transported for a long distance in suspension. This material is found only in minor quantities in the riverbed but may form a significant fraction of upper bank and floodplain deposits as the result of overbank deposition during floods (Church, 2006).

## Slide 8
Grain sizes of bed and wash material
1940
How is sediment transported?

## Slide 9
Bedload vs suspended load
From Gary Parker’s e-book
Video 1
Video 2

## Slide 10
1940
How is sediment transported? does it matter?
NOTE: I do not consider organic matter and substances that are not sediment but are part of the mud.
Grain sizes of bed and wash material

## Slide 11
The Enoree River, SC

## Slide 12
The Enoree River, SC
Soil Conservation Service field laboratory
12

## Slide 13
The Enoree River study
(Einstein et al., 1940)
Samples containing fine bank material
Very little sediment finer than 0.315 mm (42 sieve mesh) and practically no sediment finer than 0.25 mm (60 sieve mesh) was found on the channel bed. Sediment collected in traps during a storm and sediment found on the bed had similar grain size distributions

## Slide 14
The Enoree River study
(Einstein et al., 1940)
Grain size
Very little sediment finer than 0.315 mm (42 sieve mesh) and practically no sediment finer than 0.25 mm (60 sieve mesh) was found on the channel bed. Sediment collected in traps during a storm and sediment found on the bed had similar grain size distributions
Suspended load samples indicate nearly uniform distribution in the vertical for the finer sizes.
Particles coarser than 0.315 mm are found in suspension with higher concentrations near the bed

## Slide 15
The Enoree River study
(Einstein et al., 1940)
Very little sediment finer than 0.315 mm (42 sieve mesh) and practically no sediment finer than 0.25 mim (60 sieve mesh) was found on the channel bed. Sediment collected in traps during a storm and sediment found on the bed had similar grain size distributions
Suspended load samples indicate nearly uniform distribution in the vertical for the finer sizes.
Particles coarser than 0.315 mm are found in suspension with higher concentrations near the bed
The peak of suspended load precedes that of water discharge

## Slide 16
The Enoree River study
(Einstein et al., 1940)
Very little sediment finer than 0.315 mm (42 sieve mesh) and practically no sediment finer than 0.25 mm (60 sieve mesh) was found on the channel bed. Sediment collected in traps during a storm and sediment found on the bed had similar grain size distributions
Suspended load samples indicate nearly uniform distribution in the vertical for the finer sizes.
Particles coarser than 0.315 mm are found in suspension with higher concentrations near the bed
The peak of suspended load precedes that of water discharge
The suspended load consists for the 96% of sediment finer than 0.315 mm and follows a different curve than the material collected in the traps.
Trap sediment
Suspended sediment

## Slide 17
The Enoree River study
(Einstein et al., 1940)
The transport rate of particles coarser than 0.5 mm and with grain size between 0.315 mm and 0.5 mm varies in a similar way.
The transport rate of sediment with size between 0.18 mm and 0.25 mm resembles that of the silt
Sediment with grain size between 0.25 mm and 0.315 mm is a transition between the two but closer to the finest material
d > 0.315 mm
d < 0.25 mm
0.25 mm < d < 0.315 mm
Very little sediment finer than 0.315 mm (42 sieve mesh) and practically no sediment finer than 0.25 mm (60 sieve mesh) was found on the channel bed. Sediment collected in traps during a storm and sediment found on the bed had similar grain size distributions
Suspended load samples indicate nearly uniform distribution in the vertical for the finer sizes.
Particles coarser than 0.315 mm are found in suspension with higher concentrations near the bed
The peak of suspended load precedes that of water discharge
The suspended load consists for the 96% of sediment finer than 0.315 mm and follows a different curve than the material collected in the traps.

## Slide 18
Summarizing, for the Enoree River
(Einstein et al., 1940)
Sediment coarser and finer than 0.315 mm are transported with different laws;
Sediment coarser than 0.315 mm is found in abundant quantities on the bed and its transport rate seems to vary with the flow discharge

## Slide 19
Summarizing, for the Enoree River
(Einstein et al., 1940)
Sediment coarser and finer than 0.315 mm are transported with different laws;
Sediment coarser than 0.315 mm is found in abundant quantities on the bed and its transport rate seems to vary with the flow discharge
Sediment finer than 0.315 mm is contributed from the basin upstream and is transported downstream with minimum interaction with the bed, i.e. it is washed through. No relation exists between the load and the bed stress or the discharge

## Slide 20
Site-specific distinction between bed and wash material
(Einstein et al., 1940)
“Bed material composition is determined from samples taken in the bottom of the channel in the reach under consideration immediately after a flood has receded to the normal low-water stage”

## Slide 21
Site-specific distinction between bed and wash material
(Einstein et al., 1940)
“Bed material composition is determined from samples taken in the bottom of the channel in the reach under consideration immediately after a flood has receded to the normal low-water stage”
Bed material is composed of all particles that are greater than a limiting size whether moving as bedload or in suspension
Wash material composed of all particles finer than the limiting size which usually is washed into and through the reach under consideration

## Slide 22
How is bed material transported? does it matter?
Calculation of bed material load
Bulk relations estimate Einstein’s bed load, sum of the bed material transported in suspension and as bedload (it may not matter)
Different models are used to compute bedload and suspended bed material load (it matters)

## Slide 23
How is bed material transported? does it matter?
Calculation of bed material load
Bulk relations estimate Einstein’s bed load, sum of the bed material transported in suspension and as bedload (It may not matter)
Different models are used to compute bedload and suspended bed material load (it matters)
Calculation of wash load
Largely unresolved problem

## Slide 24
No, it is not
It is common practice to set the grain size separating bed material from wash material equal to 62.5 microns. Is it always true?
The limiting grain size between bed material and wash material is not necessarily equal to 62.5 microns, grain size separating sand from silt.
This limiting grain size is probably site-dependent and can be determined with field measurements.

## Slide 25
Sedimentological f scale and the y scale
Sediment sizes vary over many order of magnitudes. It is thus convenient to use a logarithmic scale to express the variability in sediment size.
The sedimentological phi (f) scale is a base-2 logarithmic scale defined as
where D is the sediment size in millimeters.

## Slide 26
Sedimentological f scale and the y scale
Sediment sizes vary over many order of magnitudes. It is thus convenient to use a logarithmic scale to express the variability in sediment size.
The sedimentological phi (f) scale is a base-2 logarithmic scale defined as
where D is the sediment size in millimeters.

## Slide 27
Sedimentological f scale and the y scale
Sediment sizes vary over many order of magnitudes. It is thus convenient to use a logarithmic scale to express the variability in sediment size.
The sedimentological phi (f) scale is a base-2 logarithmic scale defined as
where D is the sediment size in millimeters.
we have numbers that do not vary too much;
coarse sediment is associated with small numbers
This is used by people working with fine material
Sediment type | D (mm) | D (f)
Boulders | > 256 | < -8
Cobbles and pebbles | 64 ~ 256 | -8 ~ -6
Gravel | 2 ~ 64 | -6~ -1
Sand | 0.0625 ~ 2 | -1 ~ 4
Silt | 0.002 ~ 0.0625 | 4 ~ 8.9
Clay | < 0.002 | > 8.9

## Slide 28
Sedimentological f scale and the y scale
Sediment sizes vary over many order of magnitudes. It is thus convenient to use a logarithmic scale to express the variability in sediment size.
The sedimentological phi (f) scale is a base-2 logarithmic scale defined as
where D is the sediment size in millimeters.
Sediment type | D (mm) | D (f) | D (y)
Boulders | > 256 | < -8 | > 8
Cobbles and pebbles | 64 ~ 256 | -8 ~ -6 | 6 ~ 8
Gravel | 2 ~ 64 | -6 ~ -1 | 1 ~ 6
Sand | 0.0625 ~ 2 | -1 ~ 4 | 1 ~ -4
Silt | 0.002 ~ 0.0625 | 4 ~ 9 | -4 ~ -9
Clay | < 0.002 | > 9 | < -9
Numbers for sand and gravel that we can easily use.
The coarsest the grain size, the largest the diameter on the y scale

## Slide 29
Sieve analysis
Sieves
Shaker
Let’s assume that our sample weights 500 gr and the sieve opening (Db,i) are reported below
i | Db,i
 | mm
11 | 0.84
10 | 0.71
9 | 0.5
8 | 0.36
7 | 0.3
6 | 0.25
5 | 0.21
4 | 0.18
3 | 0.15
2 | 0.13
1 | 0.11
0 | PAN

## Slide 30
i | Db,i | Wretained
 | mm | gr
11 | 0.84 | 69.5
10 | 0.71 | 26.5
9 | 0.5 | 146.5
8 | 0.36 | 69.5
7 | 0.3 | 26
6 | 0.25 | 35
5 | 0.21 | 36.5
4 | 0.18 | 24.5
3 | 0.15 | 29.5
2 | 0.13 | 13.5
1 | 0.11 | 11
0 | PAN | 12
Sieve analysis
Sieves
Shaker
We measure the weight of the sediment trapped on each sieve

## Slide 31
Sieve analysis
Sieves
Shaker
We compute the weight of the sediment passing through each sieve (finer than the sieve opening)
i | Db,i | Wretained | Wpassing
 | mm | gr | gr
11 | 0.84 | 69.5 | 430.5
10 | 0.71 | 26.5 | 404
9 | 0.5 | 146.5 | 257.5
8 | 0.36 | 69.5 | 188
7 | 0.3 | 26 | 162
6 | 0.25 | 35 | 127
5 | 0.21 | 36.5 | 90.5
4 | 0.18 | 24.5 | 66
3 | 0.15 | 29.5 | 36.5
2 | 0.13 | 13.5 | 23
1 | 0.11 | 11 | 12
0 | PAN | 12 | 

## Slide 32
Sieve analysis
Sieves
Shaker
We compute the fraction of sediment finer than the sieve opening Fb,i
i | Db,i | Wretained | Wpassing | Fb,i
 | mm | gr | gr | 
11 | 0.84 | 69.5 | 430.5 | 0.861
10 | 0.71 | 26.5 | 404 | 0.808
9 | 0.5 | 146.5 | 257.5 | 0.515
8 | 0.36 | 69.5 | 188 | 0.376
7 | 0.3 | 26 | 162 | 0.324
6 | 0.25 | 35 | 127 | 0.254
5 | 0.21 | 36.5 | 90.5 | 0.181
4 | 0.18 | 24.5 | 66 | 0.132
3 | 0.15 | 29.5 | 36.5 | 0.073
2 | 0.13 | 13.5 | 23 | 0.046
1 | 0.11 | 11 | 12 | 0.024
0 | PAN | 12 |  | 

## Slide 33
Grain size distribution
The grain size distribution is described in terms of N+1 sizes Dbi (bound diameters) such that Fbi denotes the fraction of sediment that is finer than Dbi.
100 x Fb,6 = 25.4
logarithmic scale!
i | Db,i | Fb,i
 | mm | 
11 | 0.84 | 0.861
10 | 0.71 | 0.808
9 | 0.5 | 0.515
8 | 0.36 | 0.376
7 | 0.3 | 0.324
6 | 0.25 | 0.254
5 | 0.21 | 0.181
4 | 0.18 | 0.132
3 | 0.15 | 0.073
2 | 0.13 | 0.046
1 | 0.11 | 0.024

## Slide 34
i | Db,i | Fb,i
 | mm | 
11 | 0.84 | 0.861
10 | 0.71 | 0.808
9 | 0.5 | 0.515
8 | 0.36 | 0.376
7 | 0.3 | 0.324
6 | 0.25 | 0.254
5 | 0.21 | 0.181
4 | 0.18 | 0.132
3 | 0.15 | 0.073
2 | 0.13 | 0.046
1 | 0.11 | 0.024
Grain size distribution
logarithmic scale!
The finest size does not correspond to 0 (i.e. 2.4% of the sediment sample is finer than 0.11 mm).
The coarsest size does not correspond to 0.84 mm (i.e. 14% of the sample is coarser than 0.84 mm).
It is often useful to do a linear interpolation on the psi scale to determine the missing values.

## Slide 35
i | Db,i | Yb,i | Fb,i
 | mm |  | 
13 |  | ? | 1
12 | 0.84 | -0.25 | 0.861
11 | 0.71 | -0.49 | 0.808
10 | 0.5 | -1.00 | 0.515
9 | 0.36 | -1.47 | 0.376
8 | 0.3 | -1.74 | 0.324
7 | 0.25 | -2.00 | 0.254
6 | 0.21 | -2.25 | 0.181
5 | 0.18 | -2.47 | 0.132
4 | 0.15 | -2.74 | 0.073
3 | 0.13 | -2.94 | 0.046
2 | 0.11 | -3.18 | 0.024
1 |  | ? | 0
Linear interpolation on the psi scale

## Slide 36
Linear interpolation on the psi scale
i | Db,i | Yb,i | Fb,i
 | mm |  | 
13 | 1.3 | 0.38 | 1
12 | 0.84 | -0.25 | 0.861
11 | 0.71 | -0.49 | 0.808
10 | 0.5 | -1.00 | 0.515
9 | 0.36 | -1.47 | 0.376
8 | 0.3 | -1.74 | 0.324
7 | 0.25 | -2.00 | 0.254
6 | 0.21 | -2.25 | 0.181
5 | 0.18 | -2.47 | 0.132
4 | 0.15 | -2.74 | 0.073
3 | 0.13 | -2.94 | 0.046
2 | 0.11 | -3.18 | 0.024
1 |  | ? | 0

## Slide 37
Linear interpolation on the psi scale
i | Db,i | Yb,i | Fb,i
 | mm |  | 
13 | 1.3 | 0.38 | 1
12 | 0.84 | -0.25 | 0.861
11 | 0.71 | -0.49 | 0.808
10 | 0.5 | -1.00 | 0.515
9 | 0.36 | -1.47 | 0.376
8 | 0.3 | -1.74 | 0.324
7 | 0.25 | -2.00 | 0.254
6 | 0.21 | -2.25 | 0.181
5 | 0.18 | -2.47 | 0.132
4 | 0.15 | -2.74 | 0.073
3 | 0.13 | -2.94 | 0.046
2 | 0.11 | -3.18 | 0.024
1 | 0.09 | -3.45 | 0

## Slide 38
Characteristic sizes, D50, D90, Dx
DX = diameter such that X% of the sediment is finer
D50
D50 = median size
D90 = scale for the roughness height
i | Db,i | Yb,i | Fb,i
 | mm |  | 
13 | 1.31 | 0.38 | 1.00
12 | 0.84 | -0.25 | 0.86
11 | 0.71 | -0.49 | 0.81
10 | 0.50 | -1.00 | 0.52
9 | 0.36 | -1.47 | 0.38
8 | 0.30 | -1.74 | 0.32
7 | 0.25 | -2.00 | 0.25
6 | 0.21 | -2.25 | 0.18
5 | 0.18 | -2.47 | 0.13
4 | 0.15 | -2.74 | 0.07
3 | 0.13 | -2.94 | 0.05
2 | 0.11 | -3.18 | 0.02
1 | 0.09 | -3.45 | 0.00

## Slide 39
Characteristic sizes, D50, D90, Dx
DX = diameter such that X% of the sediment is finer
D50
D50 = median size
D90 = scale for the roughness height
For our sediment
D50 = 0.48 mm and D90 = 0.95 mm
i | Db,i | Yb,i | Fb,i
 | mm |  | 
13 | 1.31 | 0.38 | 1.00
12 | 0.84 | -0.25 | 0.86
11 | 0.71 | -0.49 | 0.81
10 | 0.50 | -1.00 | 0.52
9 | 0.36 | -1.47 | 0.38
8 | 0.30 | -1.74 | 0.32
7 | 0.25 | -2.00 | 0.25
6 | 0.21 | -2.25 | 0.18
5 | 0.18 | -2.47 | 0.13
4 | 0.15 | -2.74 | 0.07
3 | 0.13 | -2.94 | 0.05
2 | 0.11 | -3.18 | 0.02
1 | 0.09 | -3.45 | 0.00

## Slide 40
Characteristic diameters Di
Db,11
Fb,10
Fb,11
f10 = Fb,11- Fb,10
Di=10
i | Db,i | Yb,i | Fb,i
 | mm |  | 
13 | 1.31 | 0.38 | 1.00
12 | 0.84 | -0.25 | 0.86
11 | 0.71 | -0.49 | 0.81
10 | 0.50 | -1.00 | 0.52
9 | 0.36 | -1.47 | 0.38
8 | 0.30 | -1.74 | 0.32
7 | 0.25 | -2.00 | 0.25
6 | 0.21 | -2.25 | 0.18
5 | 0.18 | -2.47 | 0.13
4 | 0.15 | -2.74 | 0.07
3 | 0.13 | -2.94 | 0.05
2 | 0.11 | -3.18 | 0.02
1 | 0.09 | -3.45 | 0.00

## Slide 41
Characteristic diameters Di
Db,11
Fb,10
Fb,11
f10 = Fb,11- Fb,10
Di=10
Di=10 = characteristic size of sediment with grain size between Db,10 and Db,11
geometric mean
arithmetic mean
i | Db,i | Yb,i | Fb,i
 | mm |  | 
13 | 1.31 | 0.38 | 1.00
12 | 0.84 | -0.25 | 0.86
11 | 0.71 | -0.49 | 0.81
10 | 0.50 | -1.00 | 0.52
9 | 0.36 | -1.47 | 0.38
8 | 0.30 | -1.74 | 0.32
7 | 0.25 | -2.00 | 0.25
6 | 0.21 | -2.25 | 0.18
5 | 0.18 | -2.47 | 0.13
4 | 0.15 | -2.74 | 0.07
3 | 0.13 | -2.94 | 0.05
2 | 0.11 | -3.18 | 0.02
1 | 0.09 | -3.45 | 0.00

## Slide 42
Characteristic diameters Di
Db,11
Fb,10
Fb,11
f10 = Fb,11- Fb,10
Di=10
fi = volume fraction content of sediment with grain size between Db,i and Db,i+1 in the sediment sample
General form
i | Db,i | Yb,i | Fb,i
 | mm |  | 
13 | 1.31 | 0.38 | 1.00
12 | 0.84 | -0.25 | 0.86
11 | 0.71 | -0.49 | 0.81
10 | 0.50 | -1.00 | 0.52
9 | 0.36 | -1.47 | 0.38
8 | 0.30 | -1.74 | 0.32
7 | 0.25 | -2.00 | 0.25
6 | 0.21 | -2.25 | 0.18
5 | 0.18 | -2.47 | 0.13
4 | 0.15 | -2.74 | 0.07
3 | 0.13 | -2.94 | 0.05
2 | 0.11 | -3.18 | 0.02
1 | 0.09 | -3.45 | 0.00
geometric mean
arithmetic mean
Di=10 = characteristic size of sediment with grain size between Db,10 and Db,11

## Slide 43
Geometric mean diameter Dg and geometric standard deviation sg
sediment is well-sorted (uniform) when sg < 1.6
For our sediment
Dg = 0.42 mm and sg = 1.81
i | Db,i | Yb,i | Fb,i | Di | Yi | fi
 | mm |  |  | mm |  | 
13 | 1.31 | 0.38 | 1.00 | 1.05 | 0.07 | 0.14
12 | 0.84 | -0.25 | 0.86 | 0.77 | -0.37 | 0.05
11 | 0.71 | -0.49 | 0.81 | 0.60 | -0.75 | 0.29
10 | 0.50 | -1.00 | 0.52 | 0.42 | -1.24 | 0.14
9 | 0.36 | -1.47 | 0.38 | 0.33 | -1.61 | 0.05
8 | 0.30 | -1.74 | 0.32 | 0.27 | -1.87 | 0.07
7 | 0.25 | -2.00 | 0.25 | 0.23 | -2.13 | 0.07
6 | 0.21 | -2.25 | 0.18 | 0.19 | -2.36 | 0.05
5 | 0.18 | -2.47 | 0.13 | 0.16 | -2.61 | 0.06
4 | 0.15 | -2.74 | 0.07 | 0.14 | -2.84 | 0.03
3 | 0.13 | -2.94 | 0.05 | 0.12 | -3.06 | 0.02
2 | 0.11 | -3.18 | 0.02 | 0.10 | -3.32 | 0.02
1 | 0.09 | -3.45 | 0.00 |  |  | 

## Slide 44
Unimodal and bimodal grain size distributions
Using measured data, we have described our sediment sample in terms of a discrete, empirical function.
When sediment samples are not available to determine the grain size distribution, a continuous function can be used. The Gaussian (normal) distribution with mean and standard deviation s is commonly used.

## Slide 45
Unimodal and bimodal grain size distributions
Using measured data, we have described our sediment sample in terms of a discrete, empirical function.
When sediment samples are not available to determine the grain size distribution, a continuous function can be used. The Gaussian (normal) distribution with mean and standard deviation s is commonly used.
Gaussian approximation of our sediment sample
A grain size distribution that can be described with a Gaussian distribution is unimodal, as it has a single mode or peak.
The following approximations are valid for a Gaussian distribution

## Slide 46
Unimodal and bimodal grain size distributions
A sand bed river has a characteristic size of the bed surface sediment (Dsg, Ds50) that is in the sand range of sediment sizes.
The grain size distribution of many sand bed rivers are unimodal and can be reasonably approximated with a Gaussian distribution

## Slide 47
Unimodal and bimodal grain size distributions
A sand bed river has a characteristic size of the bed surface sediment (Dsg, Ds50) that is in the sand range of sediment sizes.
The grain size distribution of many sand bed rivers are unimodal and can be reasonably approximated with a Gaussian distribution
A gravel bed river has a characteristic size of the bed surface sediment (Dsg, Ds50) that is in the gravel range of sediment sizes.
The grain size distribution of many gravel bed rivers is bimodal (multimodal), with a sand mode, a gravel mode and a plateau showing a paucity of sediment in the pea-gravel range (2 mm – 8 mm).
sand mode
gravel mode
plateau

## Slide 48
Sediment fall velocity in still water
Let’s consider a spherical particle with diameter D, density rR and fall velocity vs, with R being the submerged specific gravity of the sediment and r the water density

## Slide 49
Sediment fall velocity in still water (Dietrich, 1982)
FD
Fg
Let’s consider a spherical particle with diameter D, density rR and fall velocity vs, with R being the submerged specific gravity of the sediment and r the water density
Fg = downstream impelling force of gravity
FD = resistive drag force
we want to find a relation to express fall velocity as a function of sediment and fluid properties

## Slide 50
Sediment fall velocity in still water (Dietrich, 1982)
Let’s consider a spherical particle with diameter D, density rR and fall velocity vs, with R being the submerged specific gravity of the sediment and r the water density
FD
Fg
FD = resistive drag force
Fg = downstream impelling force of gravity
cD is the drag coefficient,

## Slide 51
Sediment fall velocity in still water (Dietrich, 1982)
Let’s consider a spherical particle with diameter D, density rR and fall velocity vs, with R being the submerged specific gravity of the sediment and r the water density
FD
Fg
FD = resistive drag force
Fg = downstream impelling force of gravity
cD is the drag coefficient, and it is a function of the Reynolds number
from the e-book (chapter 6)
with n being the kinematic viscosity of water and uf the velocity of the fluid relative to the sphere.
In the case of a particle in still water uf = vs and

## Slide 52
Sediment fall velocity in still water (Dietrich, 1982)
FD
Fg
FD = resistive drag force
Condition for equilibrium Fg = FD
Let’s consider a spherical particle with diameter D, density rR and fall velocity vs, with R being the submerged specific gravity of the sediment and r the water density
Fg = downstream impelling force of gravity

## Slide 53
Sediment fall velocity in still water (Dietrich, 1982)
FD
Fg
FD = resistive drag force
Condition for equilibrium Fg = FD
simplifies into
Let’s consider a spherical particle with diameter D, density rR and fall velocity vs, with R being the submerged specific gravity of the sediment and r the water density
Fg = downstream impelling force of gravity

## Slide 54
Sediment fall velocity in still water (Dietrich, 1982)
FD
Fg
FD = resistive drag force
Condition for equilibrium Fg = FD
simplifies into
rearranging the terms
Let’s consider a spherical particle with diameter D, density rR and fall velocity vs, with R being the submerged specific gravity of the sediment and r the water density
Fg = downstream impelling force of gravity
we want to find a relation to express fall velocity as a function of sediment and fluid properties

## Slide 55
Sediment fall velocity in still water (Dietrich, 1982)
FD
Fg

## Slide 56
Sediment fall velocity in still water (Dietrich, 1982)
FD
Fg
Rep = particle Reynolds number

## Slide 57
Sediment fall velocity in still water (Dietrich, 1982)
FD
Fg
Rep = particle Reynolds number
We found a relation between the particle fall velocity and the properties of the particle and of the fluid
Relation by Dietrich (1982) without correction for particle shape
b1 | 2.891394
b2 | 0.95296
b3 | 0.056835
b4 | 0.002892
b5 | 0.000245

## Slide 58
Sediment fall velocity in still water (Dietrich, 1982)
FD
Fg
Rep = particle Reynolds number
We found a relation between the particle fall velocity and the properties of the particle and of the fluid
Relation by Dietrich (1982) without correction for particle shape
b1 | 2.891394
b2 | 0.95296
b3 | 0.056835
b4 | 0.002892
b5 | 0.000245
Another excel file, the fall velocity calculator.

## Slide 59
References
Einstein, H.A., Anderson, A..G., & Johnson, J.W. (1940) Distinction between bed-load and suspended load in natural streams. Transactions, A/merican Geophysical Union 21 (2), 628-633
Dietrich, W. E. (1982). Settling velocity of natural particles. Water Resources Research 18 (6), 1615-1626.
Church, M. (2006). Bed Material Transport and the Morphology of Alluvial River Channels. Annual Review of Earth and Planetary Science 34, 325-354.