## Slide 1
Calculation of the bed shear stress

## Slide 2
Why is this important?
Relations to predict bedload transport rates and the entrainment rate of particles either in suspension or in bedload transport are typically expressed as functions of one or two hydraulic parameters.
These parameters have traditionally been chosen to be representative of the bed shear stress .

## Slide 3
Why is this important?
Relations to predict bedload transport rates and the entrainment rate of particles either in suspension or in bedload transport are typically expressed as functions of one or two hydraulic parameters.
These parameters have traditionally been chosen to be representative of the bed shear stress .
For now, we focus on bedload transport relations.
In general, the bedload transport rate is either computed as a function of the bed shear stress or of the excess shear stress with respect to a reference value .
In most bedload transport models, the reference value (traditionally referred to as critical) is a fitting parameter. In few models it corresponds to the threshold value for the initiation of particle motion (i.e. it has a physical meaning).

## Slide 4
Why is this important?
If we want to estimate the bedload transport rate, we need to estimate the bed shear stress

## Slide 5
Why is this important?
If we want to estimate the bedload transport rate, we need to estimate the bed shear stress
Reminder (L_02.pptx)
In general, with being a non-dimensional friction coefficient and denoting the mean flow velocity
In the case of steady and uniform (normal) flow, with the acceleration of gravity, and respectively denoting the water depth (hydraulic radius in a wide cross section) and the bed slope

## Slide 6
When can we assume normal flow?
The equation expressing the conservation of bed material (the Exner equation) takes the form (see prof. Izumi’s handouts)
where is bed porosity, is bed elevation averaged over the short-term bed level changes due to bedload transport and sediment waves, is the volumetric bed material load per unit channel width (no constraints on the mode of transport), and respectively are the streamwise and temporal coordinates.

## Slide 7
When can we assume normal flow?
The equation expressing the conservation of bed material (the Exner equation) takes the form (see prof. Izumi’s handouts)
where is bed porosity, is bed elevation averaged over the short-term bed level changes due to bedload transport and sediment waves, is the volumetric bed material load per unit channel width (no constraints on the mode of transport), and respectively are the streamwise and temporal coordinates.
If I am conducting experiments to find a relation linking the bedload transport rate to the bed shear stress, I need time to measure the flow characteristics, the bed elevation and (depending on the type of flume) the bedload transport rate.
In other words, I do my measurements when the transport regime (plane bed, with bedforms …) and the average flow conditions are not changing in time, that is when there is, on average, no bed level (slope) change.
We call this condition mobile bed equilibrium (sediment is transported but the average channel bed and the flow are not changing).

## Slide 8
When can we assume normal flow?
Mathematically, the condition of mobile bed equilibrium is expressed as

## Slide 9
When can we assume normal flow?
Mathematically, the condition of mobile bed equilibrium is expressed as
Recalling that (slide 3)
The condition , corresponds to
or

## Slide 10
When can we assume normal flow?
Mathematically, the condition of mobile bed equilibrium is expressed as
Recalling that (slide 3)
The condition , corresponds to
or
not only in space (uniform) but also in time. If it were to change in time at one location (locally), the time rate of change of would have to be nonzero to drive local bed slope change and thus changes in the average flow
If is not changing in space and time, the average flow is steady and uniform (normal) and

## Slide 11
When can we assume normal flow?
Mathematically, the condition of mobile bed equilibrium is expressed as
Recalling that (slide 3)
The condition , corresponds to
or
not only in space (uniform) but also in time. If it were to change in time at one location (locally), the time rate of change of would have to be nonzero to drive local bed slope change and thus changes in the average flow
If is not changing in space and time, the average flow is steady and uniform (normal) and
Terminology reminder
Average flow here means that the flow parameters are averaged over time scales that are long compared to those typical of bed level change for bedload transport (particle entrainment or deposition – bedload video) and bedform migration (all the videos of L_03.pptx)

## Slide 12
Class project - Part 1
I prepared an excel file called FamousDatasets,xlsx and I uploaded it in the excel_files folder of the HSI repository. You should also find it in Moodle.
In this file you will find data of famous bedload transport experiments, i.e. those performed by Meyer-Peter and Muller and those performed by Gilbert.
Part 1 of the class project consists in estimating the component of the bed shear stress in these experiments that contributed to bedload transport.

## Slide 13
Class project - Part 1
I prepared an excel file called FamousDatasets,xlsx and I uploaded it in the excel_files folder of the HSI repository. You should also find it in Moodle.
In this file you will find data of famous bedload transport experiments, i.e. those performed by Meyer-Peter and Muller and those performed by Gilbert.
Part 1 of the class project consists in estimating the component of the bed shear stress in these experiments that contributed to bedload transport.
This will be done in two steps:
STEP 1: bed shear stress in laboratory flumes are affected by the presence of smooth sidewalls. The sidewall correction procedure (next slides) i s supposed to eliminate the wall effect a s far as the calculation of the bed friction i s concerned, but there is no known correction for the effect of the walls on the sediment transportation and dune configuration (Vanoni and Brooks, 1957).
STEP 2: partition of the sidewall corrected bed shear stress between skin friction (contributing to bedload transport) and form drag (not contributing to bedload transport)

## Slide 14
Procedure to remove sidewall effects from measured data
Rough bed
Smooth wall
Known parameters
Flume width B
Water discharge Q
Water depth H
Bed slope S
Sediment properties R, Dg, D50, D90
Water properties r, n
Acceleration of gravity g
Unknowns
Shear stress acting on the bed tb
Shear stress acting on the wall tw

## Slide 15
Procedure to remove sidewall effects from measured data
Rough bed
Smooth wall
Known parameters
Flume width B
Water discharge Q
Water depth H
Bed slope S
Sediment properties R, Dg, D50, D90
Water properties r, n
Acceleration of gravity g
Unknowns
Shear stress acting on the bed tb
Shear stress acting on the wall tw
Main assumptions
The cross section is divided in two non-interacting regions, the bed region and the wall region. In these regions, the streamwise component of the gravity force if balanced by the resistive force (normal flow).
Mean flow velocity U and energy gradient S are the same in the wall and in the bed region, and in the cross section.
The Darcy-Weisbach resistance relation can be applied to each region and to the cross section

## Slide 16
Procedure to remove sidewall effects from measured data
Rough bed
Smooth wall
Formulation of the problem
The wetted perimeter of the cross section P is equal to the sum of the wetted perimeters of the bed Pb and of the wall Pw regions
Equation of conservation of mass
the discharge is equal to the sum of the discharge in the bed and in the wall region
The flow velocity is the same in all regions
Equation of conservation of streamwise momentum
the downstream pull of gravity is balanced by the resistive force on the boundary
In the cross section
is the average boundary shear stress in the cross section
In the bed region
In the wall region

## Slide 17
Procedure to remove sidewall effects from measured data
Rough bed
Smooth wall
Formulation of the problem
The wetted perimeter of the cross section P is equal to the sum of the wetted perimeters of the bed Pb and of the wall Pw regions

## Slide 18
Procedure to remove sidewall effects from measured data
Rough bed
Smooth wall
Formulation of the problem
The wetted perimeter of the cross section P is equal to the sum of the wetted perimeters of the bed Pb and of the wall Pw regions
Equation of conservation of mass
the discharge is equal to the sum of the discharge in the bed and in the wall region
The flow velocity is the same in all regions

## Slide 19
Procedure to remove sidewall effects from measured data
Rough bed
Smooth wall
Formulation of the problem
The wetted perimeter of the cross section P is equal to the sum of the wetted perimeters of the bed Pb and of the wall Pw regions
Equation of conservation of mass
the discharge is equal to the sum of the discharge in the bed and in the wall region
The flow velocity is the same in all regions
Equation of conservation of streamwise momentum
the downstream pull of gravity is balanced by the resistive force on the boundary
Subtracting the equations of conservation in the bed and wall regions from the equation of conservation in the cross section it is found that
= 0

## Slide 20
Procedure to remove sidewall effects from measured data
Rough bed
Smooth wall
Formulation of the problem
The wetted perimeter of the cross section P is equal to the sum of the wetted perimeters of the bed Pb and of the wall Pw regions
Equation of conservation of mass
the discharge is equal to the sum of the discharge in the bed and in the wall region
The flow velocity is the same in all regions
Equation of conservation of streamwise momentum
the downstream pull of gravity is balanced by the resistive force on the boundary
Recalling that and that is the same in all regions

## Slide 21
Procedure to remove sidewall effects from measured data
Rough bed
Smooth wall
Formulation of the problem
The wetted perimeter of the cross section P is equal to the sum of the wetted perimeters of the bed Pb and of the wall Pw regions
Equation of conservation of mass
the discharge is equal to the sum of the discharge in the bed and in the wall region
The flow velocity is the same in all regions
Equation of conservation of streamwise momentum
the downstream pull of gravity is balanced by the resistive force on the boundary
The Darcy-Weisbach resistance relation holds in all regions

## Slide 22
Procedure to remove sidewall effects from measured data
Rough bed
Smooth wall
Formulation of the problem
The wetted perimeter of the cross section P is equal to the sum of the wetted perimeters of the bed Pb and of the wall Pw regions
Equation of conservation of mass
the discharge is equal to the sum of the discharge in the bed and in the wall region
The flow velocity is the same in all regions
Equation of conservation of streamwise momentum
the downstream pull of gravity is balanced by the resistive force on the boundary
The Darcy-Weisbach resistance relation holds in all regions
Darcy-Weisbach for pipe and open channel flow
d
H
B
r is hydraulic radius, equal to cross sectional aera over wetted perimeter

## Slide 23
Procedure to remove sidewall effects from measured data
Rough bed
Smooth wall
Formulation of the problem
The wetted perimeter of the cross section P is equal to the sum of the wetted perimeters of the bed Pb and of the wall Pw regions
Equation of conservation of mass
the discharge is equal to the sum of the discharge in the bed and in the wall region
The flow velocity is the same in all regions
Equation of conservation of streamwise momentum
the downstream pull of gravity is balanced by the resistive force on the boundary
The Darcy-Weisbach resistance relation holds in all regions
B

## Slide 24
Procedure to remove sidewall effects from measured data
Rough bed
Smooth wall
Formulation of the problem
The wetted perimeter of the cross section P is equal to the sum of the wetted perimeters of the bed Pb and of the wall Pw regions
Equation of conservation of mass
the discharge is equal to the sum of the discharge in the bed and in the wall region
The flow velocity is the same in all regions
Equation of conservation of streamwise momentum
the downstream pull of gravity is balanced by the resistive force on the boundary
The Darcy-Weisbach resistance relation holds in all regions
B
The Reynolds number or
r is replaced in the Darcy-Weisbach equations

## Slide 25
Procedure to remove sidewall effects from measured data
Rough bed
Smooth wall
Formulation of the problem
The wetted perimeter of the cross section P is equal to the sum of the wetted perimeters of the bed Pb and of the wall Pw regions
Equation of conservation of mass
the discharge is equal to the sum of the discharge in the bed and in the wall region
The flow velocity is the same in all regions
Equation of conservation of streamwise momentum
the downstream pull of gravity is balanced by the resistive force on the boundary
The Darcy-Weisbach resistance relation holds in all regions
B

## Slide 26
Friction coefficient in the wall region
Rough bed
Smooth wall
The friction coefficient in the wall region is computed with a relation for smooth pipes as function of the Reynolds number
For example, the relation by Blasius or Nikuradse for smooth pipes can be used
How to go from pipe flow to open channel flow?
Darcy-Weisbach for pipe and open channel flow
Subscripts p and oc indicate pipe and open channel, respectively
d
H
B
and

## Slide 27
Friction coefficient in the wall region
Rough bed
Smooth wall
The friction coefficient in the wall region is computed with a relation for smooth pipes as function of the Reynolds number
For example, the relations by Blasius and Nikuradse for smooth pipes can be used
How to go from pipe flow to open channel flow?
the relations by Blasius and Nikuradse for smooth boundary in open channel flow take the form
Noting that

## Slide 28
Sidewall correction calculation procedure
Rough bed
Smooth wall
Known parameters
Flume width B
Water discharge Q
Water depth H
Bed slope S
Sediment properties R, Dg, D50, D90
Water properties r, n
Acceleration of gravity g
Unknowns
Shear stress acting on the bed tb
Shear stress acting on the wall tw
Compute
Compute
Compute with a relation for smooth boundaries and
Compute and
Compute
Compute from
Compute the sidewall corrected bed shear stress as

## Slide 29
Einstein decomposition
When bedforms are not present, the drag on the bed is associated only with stresses acting tangentially to the bed (skin friction) that are responsible for transporting sediment as bedload transport.
In presence of bedforms, part of the drag (form drag) is associated with complex interaction between bedforms and flow (primarily flow separation) and does not contribute directly to bedload transport.
It is thus necessary to partition flow resistance (and bed shear stress) between skin friction and form drag to estimate values of bed shear stress for bedload transport calculations.

## Slide 30
Einstein decomposition
Let’s consider an ideal flow over a flat bed with the same microscopic roughness, energy gradient Sf and mean flow velocity U as the flow in the presence of bedforms.

## Slide 31
Einstein decomposition
Let’s consider an ideal flow over a flat bed with the same microscopic roughness, energy gradient Sf and mean flow velocity U as the flow in the presence of bedforms.
U
S = Sf
H
Equilibrium flow with bedforms (skin friction + form drag)
U
S = Sf
Hs
Ideal flow over a flat bed
(skin friction)

## Slide 32
Einstein decomposition
Let’s consider an ideal flow over a flat bed with the same microscopic roughness, energy gradient Sf and mean flow velocity U as the flow in the presence of bedforms.
U
S = Sf
H
Equilibrium flow with bedforms (skin friction + form drag)
U
S = Sf
Hs
Ideal flow over a flat bed
(skin friction)
with Cfs < Cf and Hs < H
Cfs = friction coefficient due to skin friction
Hs = water depth associated with skin friction

## Slide 33
Einstein decomposition
Let’s consider an ideal flow over a flat bed with the same microscopic roughness, energy gradient Sf and mean flow velocity U as the flow in the presence of bedforms.
U
S = Sf
H
Equilibrium flow with bedforms (skin friction + form drag)
U
S = Sf
Hs
Ideal flow over a flat bed
(skin friction)
mean bed shear stress due to bedform form drag
friction coefficient associated with form drag
mean flow depth associated with form drag
NOTE
if bedforms are present,
Cfs < Cf and Hs < H

## Slide 34
Einstein decomposition
Let’s consider an ideal flow over a flat bed with the same microscopic roughness, energy gradient Sf and mean flow velocity U as the flow in the presence of bedforms.
U
S = Sf
H
Equilibrium flow with bedforms (skin friction + form drag)
U
S = Sf
Hs
Ideal flow over a flat bed
(skin friction)
NOTE
if bedforms are present,
Cfs < Cf and Hs < H

## Slide 35
Einstein decomposition
An ideal flow over a flat bed with the same microscopic roughness, energy gradient Sf and mean flow velocity U as the flow in the presence of bedforms is considered.
U
S = Sf
H
Equilibrium flow with bedforms (skin friction + form drag)
U
S = Sf
Hs
Ideal flow over a flat bed
(skin friction)
Calculation of Cfs
we use a Manning-Strickler formulation
NOTE
if bedforms are present,
Cfs < Cf and Hs < H

## Slide 36
Einstein decomposition
An ideal flow over a flat bed with the same microscopic roughness, energy gradient Sf and mean flow velocity U as the flow in the presence of bedforms is considered.
U
S = Sf
H
Equilibrium flow with bedforms (skin friction + form drag)
U
S = Sf
Hs
Ideal flow over a flat bed
(skin friction)
The total shear velocity u*, the shear velocities associated with skin friction and form drag u*s and u*f, and the corresponding Shields numbers are
NOTE
if bedforms are present,
Cfs < Cf and Hs < H

## Slide 37
Einstein decomposition calculation procedure
Compute the grain roughness height
Determine the Chezy coefficient for the bed region and the hydraulic radius for the bed region associated with skin friction from the Keulegan and the momentum balance equations
Compute the sidewall corrected bed shear stress associated with skin friction

## Slide 38
Engelund and Hansen predictor of dune form drag
Engelund and Hansen in 1967 determined the following relation to compute form drag in presence of dunes
or
This relation is designed to be used with the following resistance relation
Chart: 
| 0.08 | 0.1 | 0.2 | 0.30000000000000004 | 0.4 | 0.5 | 0.6 | 0.7 | 0.79999999999999993 | 0.89999999999999991 | 0.99999999999999989 | 1.0999999999999999 | 1.2 | 1.3 | 1.4000000000000001 | 1.5000000000000002 | 1.6000000000000003 | 1.7000000000000004 | 1.8000000000000005 | 1.9000000000000006 | 2.0000000000000004 | 2.1000000000000005 | 2.2000000000000006 | 2.3000000000000007 | 2.4000000000000008
 | 0.06256 | 0.064 | 0.076 | 0.096 | 0.124 | 0.16 | 0.204 | 0.256 | 0.316 | 0.384 | 0.46 | 0.544 | 0.636 | 0.736 | 0.844 | 0.96 | 1.084 | 1.216 | 1.356 | 1.504 | 1.66 | 1.824 | 1.996 | 2.176 | 2.364
 | 0.08 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1 | 1.1 | 1.2 | 1.3 | 1.4 | 1.5 | 1.6 | 1.7 | 1.8 | 1.9 | 2 | 2.1 | 2.2 | 2.3 | 2.4
 | 0.06256 | 0.064 | 0.076 | 0.096 | 0.124 | 0.16 | 0.204 | 0.256 | 0.316 | 0.384 | 0.46 | 0.544 | 0.636 | 0.736 | 0.844 | 0.96 | 1.084 | 1.216 | 1.356 | 1.504 | 1.66 | 1.824 | 1.996 | 2.176 | 2.364
 | 0 | 0.04 | 0.06
 | 0.06256 | 0.064 | 0.076 | 0.096 | 0.124 | 0.16 | 0.204 | 0.256 | 0.316 | 0.384 | 0.46 | 0.544 | 0.636 | 0.736 | 0.844 | 0.96 | 1.084 | 1.216 | 1.356 | 1.504 | 1.66 | 1.824 | 1.996 | 2.176 | 2.364
 | 2.4 | 2.5 | 2.6 | 2.7 | 2.8 | 2.9 | 3 | 3.1 | 3.2 | 3.3 | 3.4 | 3.5 | 3.6 | 3.7 | 3.8 | 3.9 | 4
 | 0.06256 | 0.064 | 0.076 | 0.096 | 0.124 | 0.16 | 0.204 | 0.256 | 0.316 | 0.384 | 0.46 | 0.544 | 0.636 | 0.736 | 0.844 | 0.96 | 1.084 | 1.216 | 1.356 | 1.504 | 1.66 | 1.824 | 1.996 | 2.176 | 2.364
 | 0 | 0.04 | 0.06
no form drag
form drag

## Slide 39
Wright and Parker predictor of dune form drag
Wright and Parker in 2004 noticed that the Engelund and Hansen predictor tends to work well in the laboratory, for small and medium streams, i.e. streams in which the dune-upper plane bed transition occurs for discharges smaller than bankfull.
The Engelund and Hansen predictor does not work well in large sand bed rivers, where dunes persist at and above bankfull conditions. Wright and Parker modified it to cover small and large streams
where Fr is the Froude number
The above predictor should be used with the following resistance relation
astrat is a correction for flow stratification which can be set equal to one in absence of additional information